## Slide 1: Control/Data Separation
decouple control and data planes by providing open standard API

## Slide 2: (Logically) Centralized Controller
Controller Platform

## Slide 3: Protocols  Applications
Controller Platform
Controller Application

## Slide 4: Timescales of Data, Control, and Management Planes
 | Data | Control | Management
Time-scale | Packet (nsec) | Event (10 msec to sec) | Human (min to hours)
Tasks | Forwarding, buffering, filtering, scheduling | Routing, circuit set-up | Analysis, configuration
Location | Line-card hardware | Router software | Humans or scripts

## Slide 5: Data and Control Planes
Switching
Fabric
Processor
Line card
Line card
Line card
Line card
Line card
Line card
data plane
control plane

## Slide 6: Data Plane
Streaming algorithms on packets
  Matching on some bits
  Perform some actions
Wide range of functionality
  Forwarding
  Access control
  Mapping header fields
  Traffic monitoring
  Buffering and marking
  Shaping and scheduling
  Deep packet inspection
Switching
Fabric
Processor

## Slide 7: Switch: Match on Destination MAC
MAC addresses are location independent
  Assigned by the vendor of the interface card
  Cannot be aggregated across hosts in LAN
mac1 | 
mac2 | 
mac3 | 
mac4 | 
mac5 | 
host
host
host
...
mac1
mac2
mac3
switch
host
host
mac4
mac5

## Slide 8: Router: Match on IP Prefix
IP addresses grouped into common subnets
  Allocated by ICANN, regional registries, ISPs, and within individual organizations
  Variable-length prefix identified by a mask length
host
host
host
LAN 1
...
host
host
host
LAN 2
...
router
router
router
WAN
WAN
1.2.3.4
1.2.3.7
1.2.3.156
5.6.7.8
5.6.7.9
5.6.7.212
1.2.3.0/24
5.6.7.0/24
forwarding table
Prefixes may be nested. Routers identify the longest matching prefix.

## Slide 9: Forwarding vs. Routing
Forwarding: data plane
  Directing a data packet to an outgoing link
  Individual router using a forwarding table
Routing: control plane
  Computing paths the packets will follow
  Routers talking amongst themselves
  Individual router creating a forwarding table

## Slide 10: Example: Shortest-Path Routing
Compute: path costs to all nodes
  From a source u to all other nodes
  Cost of the path through each link
  Next hop along least-cost path to s
3
2
2
1
1
4
1
4
5
3
u
s
6
v
w
y
x
t
z

## Slide 11: Distributed Control Plane
Link-state routing: OSPF, IS-IS
  Flood the entire topology to all nodes
  Each node computes shortest paths
  Dijkstra’s algorithm
11
3
2
2
1
1
4
1
4
5
3
u
v
w
x
y
z
s
t

## Slide 12: Distributed Control Plane
Distance-vector routing: RIP, EIGRP
  Each node computes path cost
  … based on each neighbors’ path cost
  Bellman-Ford algorithm
3
2
2
1
1
4
1
4
5
3
u
v
w
x
y
z
s
t

## Slide 13: Traffic Engineering Problem
Management plane: setting the weights
  Inversely proportional to link capacity?
  Proportional to propagation delay?
  Network-wide optimization based on traffic?
3
2
2
1
1
3
1
4
5
3
3

## Slide 14: Traffic Engineering: Optimization
Inputs
  Network topology
  Link capacities
  Traffic matrix
Output
  Link weights
Objective
  Minimize max-utilized link
  Or, minimize a sum of link congestion
3
2
2
1
1
3
1
4
5
3

## Slide 15: Transient Routing Disruptions
Topology changes
  Link weight change
  Node/link failure or recovery
Routing convergence
  Nodes temporarily disagree how to route
  Leading to transient loops and blackholes
1
4
5
3
1
4
10
3
1
4
10
3

## Slide 16: Management Plane Challenges
Indirect control
  Changing weights instead of paths
  Complex optimization problem
Uncoordinated control
  Cannot control which router updates first
Interacting protocols and mechanisms
  Routing and forwarding
  Naming and addressing
  Access control
  Quality of service
  …

## Slide 22: 4D
Decision: all management and control logic
Dissemination: communicating with routers
Discovery: topology and traffic monitoring
Data: packet handling
routers
Decision
Dissemination
Discovery
Data
Network-level objectives
Direct control
Network-wide views

## Slide 23: Ethane
Higher-level policies
  Defined on principals, not network identifiers
  Language for specifying policies
Policy should dictate the paths
  Controller should select paths based on policy
Fine-grain control
  Controller handles first packet of a flow
  Data plane maintains per-flow state

## Slide 24: Practical Challenges
Scalability
  Decision elements responsible for many routers
Response time
  Delays between decision elements and routers
Reliability
  Surviving failures of decision elements and routers
Consistency
  Ensuring multiple decision elements behave consistently
Security
  Network vulnerable to attacks on decision elements
Interoperability
  Legacy routers and neighboring domains